## Slide 1
Automated lane identification using Precise Point Positioning An affordable and accurate GPS technique
Victor L. Knoop, Christian Tiberius, Peter Buist and Bart van Arem
Sponsors: Foundation Next Generation Infrastructures
IIP-CC subsidy by ICTregie/NWO

## Slide 2: Contribution
New technique for dm-accurate gps position
  Cost: ~ 100 USD
  Easy to set up
More accurate than a lane width
Automatically create maps with lane positions: proof of concept

## Slide 3: Motivation
Large focus on lateral management (cooperative active cruise control)
Lane-specific freeway advice can improve flow
Next step towards automated vehicles
2 steps: 1) find lane positions 2) determine lane of veh

## Slide 4: Regular GPS
Three dimensions => 4 satellites

## Slide 5: Errors in positions
Souces:
  (Predicted) trajectories of satellite US airforce provided
  Atmosphere
Resulting accuracy:
  ~5-10 meters horizontally
  10-20 meters vertically

## Slide 6: Differential GPS

## Slide 7: Precise Point Positioning
Hundreds of base stations
Sharing measured GPS signals
Accurate satellite trajectories (+atmospheric distortions) calculated and published
=> used to correct GPS measurement

## Slide 8: Testing
Set-up on a (small European) van
Real-life freeway test
Compare with ground truth (D-GPS)
4 sessions of each 5 runs

## Slide 9: Accuracy
Systematic for a time of day: ~50 cm off
Random: ~35 cm off
Accurate enough to identify the lane, if lane positions are known..

## Slide 10: Mapping lanes
Systematic error Normal(0;50cm)
Random error Normal(0;35 cm)
Position in vehicle Uniform(1.8m)
Vehicle position in lane Normal(0;20cm)
Lane changing 10% of the vehicles position during LC uniform over lane width
Simulation of passings

## Slide 11: Simulation results

## Slide 12: Fits of results
Estimated combined normal
  Offset (20±12cm)
  One standard deviation
  Lane distribution
  For 3-7 lanes: 3 lanes fit best

## Slide 13: Sensitivity with fewer observations
useful estimation if >100 vehicles

## Slide 14: (Practical) conclusions & future work
~100 USD receiver detecting at ~dm accuracy
Easy implementation in-car (mobile phone a bit more difficult)
Lane mapping is possible
  Many vehicles passing => Collect trajectories (openstreetmap, TomTom)
New possiblities for management and intelligent vehicles
Proof of concept shows feasibility
Now: field test for ~100 vehicles

## Slide 15: Regular GPS
One dimension => 2 satellites