## Slide 1: de Jong, Knoop, Hoogendoorn The Effect of Signal Settings on the Macroscopic Fundamental Diagram and its Applicability in Traffic Signal Driven Perimeter Control Strategies
IEEE-ITCS 2013
Session TuA8
8 October 2013, 09:18 – 09:36

## Slide 2: Overview
Introduction
Research scope
Methodology
Results
Discussion
Conclusion

## Slide 3: Introduction MFD
Relates accumulation to production
  Accumulation: average weighted density
  Production: average weighted flow
  Maximum production and optimal/critical accumulation are parameters of interest
Notes: Production and accumulation are network characteristics and are not related to the traffic within that network!

## Slide 4: Introduction
MFD can be used in perimeter control strategies
Perimeter control aims to hold back traffic in certain areas, in order to maximize production in another area
One method to achieve this is by changing signal timings
Research has found that changing signal timings changes the shape of the MFD
Studies aiming to implement perimeter control, have not taken this effect into account yet

## Slide 5: Research scope
In what way do changes in traffic light settings at the arterial around a subnetwork, influence the shape of the MFD of the subnetwork and the arterial itself

## Slide 6: Methodology Simulation setup
Simulation model (VISSIM):
  Detailed node model
  Individual signal timings for each intersection (static)
  Rerouting possible
Network and OD-matrix (Matlab):
  Randomly generated street pattern and OD matrix in 3x3 km network
  Network layout and signal timings are tuned to demand
Simulations:
  First simulations are run in order to construct a ‘basic’ MFD
  Next simulations are run using different signal timings

## Slide 7: Methodology Inflow and outflow control
Inflow control: Signal timings for flow from arterial to subnetwork are fixed to accommodate specific number of vehicles (100, 200, 300, 400, 500)
Outflow control: Signal timings for flow from subnetwork to arterial are fixed
Subnetwork
Aterial

## Slide 8: Results Controlling subnetwork inflow
Different signal timings result in differently shaped MFDs
Improvement in production for subnetwork found at 200-400 veh/h
Certain productions can be sustained over a large accumulation range
30.000 vehicles completing trip at 100 veh/h, in other cases 15.000 - 20.000

## Slide 9: Results Controlling subnetwork outflow
Roughly same results as for controlling inflow
Timings at which highest production is achieved (300-500), differs from inflow (200-400)
32.000-35.000 vehicles completing trip at 400-500, in other cases 25.000

## Slide 10: Discussion Improvements in traffic flow
Improvements can be achieved over locally optimized signals
Highest production does not always result in highest output
Production of perimeter is higher than subnetwork
For both control strategies output is maximized if as many vehicles as possible are kept within the perimeter
  The perimeter is better capable in processing traffic and preventing gridlock
  Formation of ‘gridblocks’ in subnetwork easier

## Slide 11: Discussion Critical accumulation
Accumulation at which production is maximized differs, given different signal timings
Using critical accumulation of the original MFD as a control target results in a different (possibly lower) critical accumulation, resulting in even more congestion
A-priori construction of MFDs for different signal timings needed

## Slide 12: Conclusion
For two control types tested, no substantial differences in maximum production are found. However, higher outputs achieved with outflow control
Keeping the perimeter at maximum production and keeping amount of traffic in subnetwork low generates best results
Production can improve by changing signal timings
Different signal timings can have a strong effect on the shape of the MFD, i.e. the maximum production and critical accumulation
As critical accumulation differs for different signal timings, it cannot be directly utilized input for control strategies
A-priori construction of MFD for different signal timings needed for (perimeter) control strategies

## Slide 13: Questions?