## Slide 1
Single Frequency Precise Point Positioning:
obtaining a map accurate to lane-level
Victor L. Knoop, Peter de Bakker, Christian Tiberius, and Bart van Arem
NWO – There is plenty of lane in the other lane

## Slide 2: Contribution
New technique for dm-accurate gps position
  Cost: ~ 100 USD
  Easy to set up
More accurate than a lane width
Automatically create maps with lane positions: field test

## Slide 3: Motivation
Large focus on lateral management (cooperative active cruise control)
Lane-specific freeway advice can improve flow
Next step towards automated vehicles
2 steps: 1) find lane positions 2) determine lane of veh

## Slide 4: Regular GPS
Three dimensions => 4 satellites
Resulting accuracy:
  ~5-10 meters horizontally
  10-20 meters vertically

## Slide 5: Differential GPS
Resulting accuracy:
  < 1cm
High cost

## Slide 6: Precise Point Positioning
Hundreds of base stations
Sharing measured GPS signals
Accurate satellite trajectories (+atmospheric distortions) calculated and published
=> used to correct GPS measurement
Accuracy: ~1-2 dm
Cost: regular GPS (~100 USD)

## Slide 7: Field test set up
100 rounds of 2 X 5km freeway stretch
PPP and D-GPS (reference)

## Slide 8: Accurary
Not bias free (due to construction on roof?): 20 cm off
Typical error: 20 cm

## Slide 10: Fits
Fit the frequency of passing at a lateral position
Combined normal distributions

## Slide 11: Combine 10 cross sections
Increase data sample
Only works for the same road layout (laterally)

## Slide 12: (Practical) conclusions & future work
~100 USD receiver detecting at ~dm accuracy
Easy implementation in-car (mobile phone a bit more difficult)
Lane mapping is possible
  100 vehicles passing => Collect trajectories (openstreetmap, TomTom)
New possiblities for management and intelligent vehicles
Field operational test shows feasibility
Next:
  integration in commercial devices
  More challanging conditions